## Slide 1: MORDM using Rhodium The lake problem workflow
Antonia Hadjimichael
Reed Group Meeting
July 31, 2019
Notes: Overarching Theme of Research – 5 min
Lake Problem work so far – 10 min
Red River work so far – 10 min
Papers/studies (<= 10 min)
  Lake study
  Policy diagnostic on Red River
  Expand information in policies and explore robustness to climate change
Back-up slides anticipating questions

## Slide 2: Disclaimer and additional info
This training is meant to guide you on the what and why of MORDM using the lake problem. There is a lot of material others have written which I will be reusing because there is no point in reinventing the wheel:
Julie’s GH repository for the system
Julie’s paper
Dave Hadka’s Rhodium example scripts (that I modified)
A lot of these slides have also been prepared by others (Julie Quinn, Jon Herman, Tori Ward, Dave Gold)
The scripts and data I’ll be referring to here can be downloaded from this repository

## Slide 3: Learning outcomes of this training
Use Rhodium for:
  Optimization to generate alternatives
  Exploratory modeling for multiple states of the world
  Assess the robustness of candidate solutions
  Sensitivity analysis to identify key factors for failure
Highlight the importance of these steps in the context of MORDM
Demonstrate the value of Direct Policy Search (DPS)
Investigate the challenges posed by nonlinear tipping points

## Slide 4: Many-Objective Robust Decision Making (MORDM)
Exploratory modeling framework
Investigate the response of alternative management plans to a wide range of deeply uncertain states of the world (SOWs)

## Slide 5: Taxonomy of robustness frameworks
Herman et al. (2015)
https://doi.org/10.1061/(ASCE)WR.1943-5452.0000509

## Slide 6
Python library capable of:
  Multi-objective Optimization
  Exploratory Modeling
  Scenario Discovery
  Global Sensitivity Analysis
Fortran
Rhodium Robust Decision Making
Acts as the “glue” between your model and analysis codes
  Connects to models in C, C++, Fortran, Excel, R, Python
Dave Hadka,
Developer

## Slide 7: The Shallow Lake Problem
Slide credit: Tori Ward
P Recycled in the Lake
Environmental and Economic Objectives are in Direct Conflict
Notes: Notes on Lake Problem choice: It is one of the most popular tipping point benchmark problems to emerge from environmental decision-making literature.
It has a rich conceptualization that allows for exploration of challenging management and mathematical traits with relatively modest computational demands.

## Slide 8: MORDM using Rhodium The lake problem workflow

## Slide 9: MORDM using Rhodium The lake problem workflow
Difficult to identify effective policies:
High dimensional decision space for candidate actions (one action per timestep)
Weak system response to decisions at the end of the study period
Non-linear threshold
Use of Direct Policy Search (DPS):
Closed loop control
Map system states to decisions
Result in a policy, not a sequence of actions

## Slide 10
10
Let = Mass of P in the lake
Then the flux of P, can be modeled by the following equation:
Model of lake dynamics
Notes: Discuss reversible, hysteretic, and irreversible lakes and mention that this study focused on irreversible lakes.

## Slide 11
11
P Sinks
Model of lake dynamics
Anthropogenic P Inputs
Natural P Inputs
Recycled P
Fluxes of P
Notes: Discuss reversible, hysteretic, and irreversible lakes and mention that this study focused on irreversible lakes.

## Slide 12: Model of lake dynamics
12
Fluxes of P
Outputs
Equilibrium
Inputs
Notes: Discuss reversible, hysteretic, and irreversible lakes and mention that this study focused on irreversible lakes.

## Slide 14
Direction of Attraction

## Slide 15
Healthy, Oligotrophic Equilibrium
Unhealthy, Eutrophic Equilibrium
Direction of Attraction

## Slide 16
Healthy, Oligotrophic Equilibrium
Unhealthy, Eutrophic Equilibrium
Direction of Attraction
Tipping Point

## Slide 17: Why is this important?
We’re trying to decide on the values of that maximize our economic benefits, but also increase P in the lake
Increase P too much, and we cross a tipping point of no return
This value of P is hard to know exactly from before because:
Depends on stochastic
Rate of inputs is non-linear
System parameters might be (deeply) uncertain

## Slide 18: Multi-objective formulation of the Lake Problem
Objective 1:
Objective 3:
Objective 2:
Objective 4:
Maximize Expected Economic Benefits
Minimize Maximum P Concentration
Maximize Inertia (Measure of Stability)
Maximize Reliability (Fraction of Years Below Threshold)
Notes: Describe each objective and how it is calculated. The lake problem hopes to maximize economic benefit while minimizing Phosphorus concentrations in the lake by deciding how much to pollute in each time step. Economic Benefit is the expected benefit. Phosphorus in the lake is a minimization of the maximum expected phosphorus in each time step. This formulation involves one hundred time steps. In each time step, the town may alter its Phosphorus load. There is an inertia objective to minimize the number of time steps in which the town decreases its phosphorus load by more than 20% of the maximum possible range. Reliability is calculated as the total number of times the lake does not flip over all time steps and states of the world. In this formulation, the threshold is known, making the problem substantially easier than it could be.
There was a reliability constraint that reliability must remain above 85%. This is substantially less risk averse than many real-world managers would be.
Mention all of the analogous environmental threshold problems. Also mention that these are just one possible abstraction of values related to an uncertain threshold.

## Slide 19: Solution strategies
Open loop control (Intertemporal)
  Each candidate solution is a set of decision variables , representing the anthropogenic discharges at each timestep
  100 decision variables
Closed loop control (DPS)
  Each candidate solution is a control rule
  mapping the current P concentration, , to
  a decision
  6 decision variables
This figure can be replicated by running this script

## Slide 20: Model formulation in Rhodium General template for creating a Rhodium model
from rhodium import *
def model_name(array_of_levers, array_of_model_parameters):
return(array_of_model_responses)
model = Model(model_name)
model.parameters = [Parameter(“parameter_name1"),
Parameter(“parameter_name2")]
model.responses = [Response(“system_objective1”, Response.MINIMIZE),
Response(“system_objective2”, Response.MAXIMIZE),
Response(“system_objective3”, Response.INFO)]
model.constraints = [Constraint(" system_objective3 >= 0.8")]
model.levers = [RealLever("array_of_levers", 0.0, 0.1, length=100)]
model.uncertainties = [UniformUncertainty("parameter_name1", 0.0, 5.00),
UniformUncertainty("parameter_name2", 2.0, 8.5)]
output = optimize(model, "NSGAII", 10000)
parameters of interest
model responses or outputs
constraints that must be satisfied
parameters we have control over (levers)
parameters representing exogeneous uncertainties
system model as a function

## Slide 21: Model formulation in Rhodium 1. Open loop control (Intertemporal)
import math
import numpy as np
import matplotlib as mpl
import matplotlib.pyplot as plt
from scipy.optimize import brentq as root
from rhodium import *
# Construct the lake problem
def lake_problem(pollution_limit,
b = 0.42, # decay rate for P in lake (0.42 = irreversible)
q = 2.0, # recycling exponent
mean = 0.02, # mean of natural inflows
stdev = 0.001, # standard deviation of natural inflows
alpha = 0.4, # utility from pollution
delta = 0.98, # future utility discount rate
nsamples = 100): # monte carlo sampling of natural inflows
#Body of function
return (max_P, utility, inertia, reliability)
Script can be found here

## Slide 22: Model formulation in Rhodium 1. Open loop control (Intertemporal)
model = Model(lake_problem)
model.parameters = [Parameter("pollution_limit"),
Parameter("b"),
Parameter("q"),
Parameter("mean"),
Parameter("stdev"),
Parameter("delta")]
model.responses = [Response("max_P", Response.MINIMIZE),
Response("utility", Response.MAXIMIZE),
Response("inertia", Response.MAXIMIZE),
Response("reliability", Response.MAXIMIZE)]
model.constraints = [Constraint("reliability >= 0.95")]
model.levers = [RealLever("pollution_limit", 0.0, 0.1, length=100)]
model.uncertainties = [UniformUncertainty("b", 0.1, 0.45),
UniformUncertainty("q", 2.0, 4.5),
UniformUncertainty("mean", 0.01, 0.05),
UniformUncertainty("stdev", 0.001, 0.005),
UniformUncertainty("delta", 0.93, 0.99)]
Script can be found here
Define all parameters to the model that we will be studying
Define the model outputs
Define any constraints (can reference any parameter or response)
Some parameters are levers that we control via our policy
Some parameters are exogenous uncertainties

## Slide 23: Model formulation in Rhodium 1. Open loop control (Intertemporal)
setup_cache(file="example.cache")
output = cache("output", lambda: optimize(model, "NSGAII", 10000))
Script can be found here
Without using the cache, execute with simply:
output = optimize(model, "NSGAII", 25000)
We can use cache to store intermediate results and also reuse them later without having to rerun the optimization
To store outputs:
output.save("output.csv")
To store only objectives:
output.as_dataframe()[list(model.responses.keys())].to_csv('output_objectives.csv')
To load:
output = load('output.csv')[1]

## Slide 24: Model formulation in Rhodium 2. Closed loop control (DPS)
import math
import numpy as np
import matplotlib as mpl
import matplotlib.pyplot as plt
from scipy.optimize import brentq as root
from rhodium import *
# Construct the lake problem
def lake_problem_dps(policy, # the DPS policy
b = 0.42, # decay rate for P in lake (0.42 = irreversible)
q = 2.0, # recycling exponent
mean = 0.02, # mean of natural inflows
stdev = 0.001, # standard deviation of natural inflows
alpha = 0.4, # utility from pollution
delta = 0.98, # future utility discount rate
nsamples = 100, # monte carlo sampling of natural inflows
steps = 100): # the number of time steps (e.g., days)
#Body of function
return (max_P, utility, inertia, reliability)
Script can be found here

## Slide 25: Model formulation in Rhodium 2. Closed loop control (DPS)
dps_model = Model(lake_problem_dps)
dps_model.parameters = [Parameter("policy"),
Parameter("b"),
Parameter("q"),
Parameter("mean"),
Parameter("stdev"),
Parameter("delta")]
dps_model.responses = [Response("max_P", Response.MINIMIZE),
Response("utility", Response.MAXIMIZE),
Response("inertia", Response.MAXIMIZE),
Response("reliability", Response.MAXIMIZE)]
dps_model.constraints = [Constraint("reliability >= 0.95")]
dps_model.levers = [CubicDPSLever("policy", length=3)]
dps_model.uncertainties = [UniformUncertainty("b", 0.1, 0.45),
UniformUncertainty("q", 2.0, 4.5),
UniformUncertainty("mean", 0.01, 0.05),
UniformUncertainty("stdev", 0.001, 0.005),
UniformUncertainty("delta", 0.93, 0.99)]
Script can be found here
Define all parameters to the model that we will be studying
Define the model outputs
Define any constraints (can reference any parameter or response)
This strategy uses a DPS function as a lever
Some parameters are exogenous uncertainties

## Slide 26: Model formulation in Rhodium 2. Closed loop control (DPS)
setup_cache(file="dps_example.cache")
dps_output = cache("dps_output", lambda: optimize(model, "NSGAII", 10000))
Script can be found here
We can use cache to store intermediate results and also reuse them later without having to rerun the optimization
Without using the cache, execute with simply:
dps_output = optimize(model, "NSGAII", 25000)
To store outputs:
dps_output.save("dps_output.csv")
To store only objectives:
dps_output.as_dataframe()[list(dps_model.responses.keys())].to_csv('dps_output_objectives.csv')
To load:
dps_output = load('dps_output.csv')[1]

## Slide 27: Note:
This optimization can also be run with Borg (as was done in the paper).
This is still a beta version functionality of Project Platypus but to do so, download wrappers.py and place it in the platypus repository system files.
Rerun “python setup.py install”.
You’ll also need the Borg C files in the same directory.
To run, add this to the top of your code:
from platypus import wrappers
And run with this command instead:
optimize(model, "BorgMOEA", 20000, module="platypus.wrappers", epsilons=[0.01, 0.01, 0.0001, 0.0001])

## Slide 28: Exploring tradeoffs with Rhodium
To explore the two sets of candidate strategies using the tools provided by Rhodium, we need to merge them into a single dataset. We can do so by adding a key to each solution identified by each strategy:
for i in range(len(output)):
output[i]['strategy']=1
for i in range(len(dps_output)):
dps_output[i]['strategy']=0
merged = DataSet(output+dps_output)

## Slide 29: Exploring tradeoffs with Rhodium
We can visualize the two sets with J3.
We’d need to import it first with: from j3 import J3
J3(merged.as_dataframe(list(model.responses.keys())+['strategy']))

## Slide 30: Exploring tradeoffs with Rhodium
DPS
Intertemporal

## Slide 31: Why is this important?
The results indicate that the DPS strategy was able to find more 49 non-dominated solutions whereas the intertemporal strategy found 25 (running Borg for 20000 NFE).
Multiple DPS solutions outperform intertemporal solutions in every objective.
In other words, DPS is able to find solutions that achieve higher economic benefits at lower P concentrations and higher reliability and inertia.

## Slide 32: Investigating specific solutions
DPS solution with highest economic benefits
DPS solution with highest reliability

## Slide 33: Investigating specific solutions
Intertemporal solution with highest economic benefits
Intertemporal solution with highest reliability

## Slide 34: Note:
Doing the analysis in this manner, keeps all solutions found between the two strategies. Some of these solutions might be dominated by solutions found using the other strategy.
We can sort all solutions for non-dominance and generate an overall set of non-dominated solutions.
To do so one can use pareto.py. Save in the same directory and run:
python pareto.py ./*output_objectives.csv -o 1-4 -e 0.01 0.01 0.001 0.001 --header 1 --output overallreference.csv --delimiter="," --comment="#" --contribution --maximize 1 3-4
colnames = ['sol_no']+list(dps_model.responses.keys())+['strategy']
merged_sorted = load('overallreference.csv', names=colnames)[1]
To load and continue the analysis with this set run:

## Slide 35: Robustness Assessment
Evaluated the performance of Intertemporal and DPS solutions on 1,000 Latin hypercube samples of parameter values, or “States of the World” (SOWs):
Parameter | Base Value | Minimum | Maximum
b | 0.42 | 0.1 | 0.45
q | 2 | 2.0 | 4.5
µ | 0.03 | 0.01 | 0.05
σ | √10-5 ≈ 0.003 | 0.001 | 0.005
X0 | 0 | 0 | 0.3
δ | 0.98 | 0.93 | 0.99

## Slide 36: Robustness Assessment
Evaluated the performance of Intertemporal and DPS solutions on 1,000 Latin hypercube samples of parameter values, or “States of the World” (SOWs):
Parameter | Base Value | Minimum | Maximum
b | 0.42 | 0.1 | 0.45
q | 2 | 2.0 | 4.5
µ | 0.03 | 0.01 | 0.05
σ | √10-5 ≈ 0.003 | 0.001 | 0.005
X0 | 0 | 0 | 0.3
δ | 0.98 | 0.93 | 0.99
For each point in the Pareto set, we find the fraction of the 1,000 SOWs in which:
Average Economic Benefits > 0.2 AND Average Reliability > 95%

## Slide 37: Assessing robustness with Rhodium
We have already defined our exogenous uncertainties:
model.uncertainties = [UniformUncertainty("b", 0.1, 0.45),
UniformUncertainty("q", 2.0, 4.5),
UniformUncertainty("mean", 0.01, 0.05),
UniformUncertainty("stdev", 0.001, 0.005),
UniformUncertainty("delta", 0.93, 0.99)]
We now need to sample them:
SOWs = sample_lhs(model, 1000)
And reaevalute all identified solutions under all the sampled SOWs:
reevaluation = [evaluate(model, update(SOWs, policy)) for policy in output]
reevaluation_dps = [evaluate(dps_model, update(SOWs, policy)) for policy in dps_output]
This will take a while to run

## Slide 38: Average Reliability > 95% and Average Economic Benefits > 0.2

## Slide 39: What’s driving these failures?

## Slide 40: Let’s look at the most robust DPS solution

## Slide 41: Let’s look at the most robust DPS solution

## Slide 42: Let’s look at the most robust DPS solution
Optimized to a world in which critical P threshold = 0.54, approximate failure threshold

## Slide 43: Let’s look at the most robust DPS solution
Optimized to a world in which critical P threshold = 0.54, approximate failure threshold
Including information on estimated b and q into the DPS policy (and updating this through endogenous learning) could improve robustness